## Slide 1: Technical System

## Slide 2: Experimental Modeling
Training
Algorithm

## Slide 3: Anwendung: Diesel-Motordatensatz
Modell
yi = f (xi, ui) + Fehler
Störungen - ui
6 Eingänge - xi
Drehzahl in 1/min
Drehmoment in Nm
Einspritzbeginn in °CA
AGR-Rate in %
Ladedruck in kPa
Raildruck in MPa
NOx in ppm
mNOx_F in g/h
Soot in FSN
mRussFSN in g/h
CO in ppm
mCO in g/h
THC in ppm
Beff in g/kWh
TAbgvT in °C
9 Ausgänge- yi
Trainingsdaten = 193 Messpunkte
Validierungsdaten = 12 Messpunkte

## Slide 4: B-Pillar Metamodel
Technical and Economical Analysis of a B-Pillar
  Technical analysis
    Leightweight quality for defined load scenario
    Finite Element Method (FEM) simulation utilized (~5 minutes per simulation)
  Economical analysis
    Manufacturing costs
  Design parameters
    See b-pillar’s cross-section below (4 inputs)
B-Pillar in detail
Constant
deformation of
5 mm
Load scenario
thickness t
width b
height h
E-Modulus
z
y
x
z
y
x

## Slide 5: B-Pillar Metamodel Generation
Konstruktionsvariante
Local Model Network
Overal Result
Design Parameter
Technical- and Economical Analysis
€
+
+
+
+
Training
B-Pillar Designs
4 dimensional input space
600 training data samples
Latin hypercube distributed
Training time: ~ 6 seconds

## Slide 6: B-Pillar Metamodel Application
Konstruktionsvariante
Local Model Network
Optimization
Design Parameter
Application
B-Pillar Designs

## Slide 7: B-Pillar Metamodel Application Results
Pareto-Front Identification
  Procedure
  Minima and maxima for each input defined
  30 equally spaced values per input-axis  304 = 810.000 b-pillar designs
  Technical and economical analysis with local model network  0.6 seconds for 810.000 evaluations (CPU: 2.2 GHz x 4, RAM: 8 GB)
  Work-in-progress
    Validation of LMN with FEM simulations for specific b-pillar designs
    Sensitivity analysis of design parameters
Leightweight quality
Production costs

## Slide 8: Centrifugal Fan Metamodel
Efficiency Optimization of Centrifugal Fans
  Computational fluid dynamics (CFD) simulations utilized (~4 hours per simulation)
  Target values
    Pressure curve and efficiency curve
  Design parameters
    Number of blades, inner and outer diameter, several angles, etc.
Inputs: 9 Geometric parameters
Outputs: pressure, efficiency
CFD

## Slide 9: Centrifugal Fan Geometry Parameter
 | Parameter | 
1 | Inner diameter | D1/D2
2 | Inlet blade width | b1/D2
3 | Outlet blade width | b2/D2
4 | Inlet blade angle | bS1
5 | Outlet blade angle | bS2
6 | Number of blades | z
7 | Blade inclination | d
8 | Front edge angle | l
9 | Nozzle radius | rD/D1

## Slide 10: Centrifugal Fan Metamodel Generation
Local Model Network
Results
Design Parameter
Training
CFD Simulations
Centrifugal Fan Designs
9 dimensional input space
Planned ~3000 training data samples
Latin hypercube distributed + active learning strategy with HILOMOTDoE

## Slide 11: Centrifugal Fan Metamodel Application
Local Model Network
Optimization
Design Parameter
Application
Centrifugal Fan Designs

## Slide 12: Mass Air Flow (MAF) Prediction
Prediction of Mass Air Flow (MAF)
    Needed to determine optimal amount of fuel such that λ = 1
    Calculated on the engine control unit (ECU)
MAF: Mass air flow
MAP: Intake manifold air pressure
N: Engine speed
CAM_IN: Variable valve timing for intake camshaft
CAM_EX: Variable valve timing for exhaust camshaft
PORT: Actuator settings of swirl flap
VIM: Actuator settings of variable intake manifold
Notes: Swirl flap – Drallklappe
Variable intake manifold - Schaltsaugrohr

## Slide 13: Mass Air Flow (MAF) Input Selection
Available Data Set
    Total number of samples after deletion of outliers: N = 3045
    Number of physical inputs: dim = 6
    Total number of training samples: NT = 2589
    Total number of test samples: NG = 456
Substitution
Input Selection
Wrapper Approach
Backward elimination
AICc
Separated x-z selection

## Slide 14: Climate Control
2 controlled inputs (u1, u2)
  - valve positions
4 measured inputs (d1, d2, d3, d4)
    - temperature, rel. humidity, temp., temp.
2 measured outputs (y1, y2):
  - temperature, rel. humidity
87000 data samples (dynamic) in ~24h (T0=1s)
Difficult modeling with ARX: Unstable models are possible
Process